## Slide 1: Piano Room Device
Louis Hu, Drew Council, Haseeb Chaudhry, Ricky Weerts

## Slide 2: Motivation

## Slide 3: Problem Statement
No way to find out if piano room is open remotely
Needs a system to allow users to check whether any rooms are available

## Slide 4
Key Results
Physical Circuitry
Software
Front-end
Back-end
Casing
Sensor
Microcontroller

## Slide 5: Design Objectives and Constraints
Objectives, Constraints | Target Value
Durability (objective) | >= 2-3 years, maintenance < every 6 months
Accessibility (objective) | Easier to use than physically going there, survey score > 8/10
Compatibility (constraint) | Works with IOS, Android, and Computers
Aesthetics (objective) | Approval rating > 80%. Hidden Wiring
Precision (objective) | Detection time < 2-3 minutes
Privacy (constraint) | Privacy rating > 95%. No Privacy Laws violated
Accuracy (objective) | False alarms < Failures to detect

## Slide 6
Correct | Type 1 Error False Alarms
Type 2 Error Failure to Detect | Correct
YES
NO
Detected
YES
NO
Person is in the Room
Accuracy

## Slide 7: Design Solution Ideas
PIR - Detects change in infrared radiation coming from objects in view
Ultrasonic - Uses sound waves to detect the distance from objects in a room
Temporal camera - Takes pictures of the room and compares pictures for differences over time
Body/face detection - Uses facial recognition technology to identify when a face or body is in the room

## Slide 8: Pugh Scoring for Detection
 | Weight | PIR | Light Detection | Body/face detection | Temporal Camera | Background Compare | Ultrasonic | IR Camera
Accessibility | 0.0 | 3 | 3 | 3 | 3 | 3 | 3 | 3
Accuracy | 0.4 | 5 | 5 | 4 | 3 | 4 | 4 | 4
Compatibility | 0.0 | 3 | 3 | 3 | 3 | 3 | 3 | 3
Durability | 0.3 | 5 | 5 | 1 | 4 | 2 | 5 | 3
Precision | 0.25 | 3 | 1 | 5 | 4 | 5 | 3 | 4
Aesthetics | 0.05 | 4 | 5 | 1 | 3 | 3 | 4 | 3
Total | 1 | 4.45 | 4 | 3.2 | 3.55 | 3.6 | 4.05 | 3.65
RANK |  | 1 | 3 | 7 | 6 | 5 | 2 | 4

## Slide 9: Pugh Scoring for Detection
 | Weight | PIR | Light Detection | Body/face detection | Temporal Camera | Background Compare | Ultrasonic | IR Camera
Accessibility | 0.0 | 3 | 3 | 3 | 3 | 3 | 3 | 3
Accuracy | 0.4 | 5 | 5 | 4 | 3 | 4 | 4 | 4
Compatibility | 0.0 | 3 | 3 | 3 | 3 | 3 | 3 | 3
Durability | 0.3 | 5 | 5 | 1 | 4 | 2 | 5 | 3
Precision | 0.25 | 3 | 1 | 5 | 4 | 5 | 3 | 4
Aesthetics | 0.05 | 4 | 5 | 1 | 3 | 3 | 4 | 3
Total | 1 | 4.45 | 4 | 3.2 | 3.55 | 3.6 | 4.05 | 3.65
RANK |  | 1 | 3 | 7 | 6 | 5 | 2 | 4

## Slide 10: Design Sketch

## Slide 11: Sensor Prototype
PIR Sensor
LCD Display
Example Output

## Slide 12: Website Prototype
Visiting a link (below), updates data on the site to show the occupancy of the rooms (right)
Update Data Page
View Data Page

## Slide 13
Key Results
Physical Circuitry
Software
Website
(Front-end)
Python
(Back-end)
Raspberry Pi
(Micro-
controller)
PIR & Ultrasonic Sensor
(Sensors)
Acrylic/3D Print
(Casing)

## Slide 14: Future Plans
Continue testing sensors and identify a configuration that works well for the room
Jam Session button
Improve website aesthetics
Get sensor circuit to connect to website
Perform testing to check the efficacy of our design

## Slide 15: Conclusion
A system using PIR and Ultrasonic sensors to detect the presence of people and update a website accordingly
Will save piano users valuable time in checking the occupancy of piano rooms and increase efficiency of piano room usage

## Slide 16: Acknowledgements
Dr. Rizk, Dr. West
Writing Consultant: Annie
Technical Mentor: Dr. Teng Su
TA: Will Inigo
Client: Catherine McMillan